## Slide 1: Data Link Layer: Part I
Data Link Layer Functions
  deliver frames over a single link
  framing, media access, error checking (error correction), …
Local Area Networks (LANs) and MAC Addresses
  MAC addresses (vs. IP address)
  point-to-point vs. shared access
  IP Address Resolution Protocol (ARP) and IP datagram forwarding (revisited!)
Extending LANs & Switched LANs:
  Self-learning
  Spanning tree algorithms
Readings: Textbook, Chapter 6: Sections 6.1 and 6.4.1-6.4.3

## Slide 2: Data Link Layer: Introduction
Some terminology:
hosts and routers are nodes
(bridges and switches too)
communication channels that connect adjacent nodes along communication path are links
  wired links
  wireless links
  LANs (local area networks)
layer 2 PDU (“packet”) referred to as frame, which encapsulates a layer-3 packet, e.g., an IP datagram
“link”

## Slide 3: What Does Data Link Layer Do?
An IP packet from host A to host B may traverses different links using different data link protocols
  e.g., Ethernet on first link, frame relay on intermediate links, 802.11 on last link
Each link protocol provides different services
  e.g., may or may not provide reliable data delivery
Different link protocols are not inter-operable!
  IP packets are encapsulated/decapsulated with appropriate data link protocol header over each link
  IP protocol and IP routers glue the links (“physical networks”) together and provide end-to-end data delivery!
Data link layer has responsibility of
transferring frames from one node to adjacent node over a single link

## Slide 4: Data Link Layer Functions
Framing
  sender (transmitter): encapsulate datagram into frame, adding header, trailer, transmit frame
  receiver: detect beginning of frames, receive frame, decapsulate frame, stripping off header, trailer
Link Access (Media Access Control)
  determine whether it’s Okay to transmit over the link
    particularly important when link shared by many nodes
      also an issue over “half-duplex” point-to-point link (why?)
    need media access control (MAC)
  “physical addresses” identify sender/receiver on a link!
    particularly important when link shared by many nodes, while over point-to-point link, not necessary
    “physical addresses” often referred to as “MAC” addresses
      different from IP addresses (which are logical & global)!

## Slide 5: Other Data Link Layer Functions
Error Detection (commonly implemented)
  errors caused by signal attenuation, noise, etc.
  sender computes “checksum”, attaches to frame
  receiver detects presence of errors by verifying “checksum”
    drops corrupted frame, may ask sender for retransmission
  Commonly used “checksum”: cyclic redundancy code (CRC)
Reliable delivery between adjacent nodes (optional)
  using, e.g., go-back-N or selective repeat protocol
    seldom used on low bit error link (fiber, some twisted pair)
    wireless links: high error rates
    Q: why both link-level and end-end reliability?
Error Correction (optional)
  receiver identifies and corrects bit error(s) without resorting to retransmission, using forward error correction (FEC) codes
Flow Control (optional)
  negotiating transmission rates between two nodes

## Slide 6: Where is the link layer implemented?
in each and every host
link layer implemented in “adaptor” (aka network interface card NIC) or on a chip
  Ethernet card, 802.11 card; Ethernet chipset
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network adapter
card
application
transport
network
link
link
physical

## Slide 7: Adaptors Communicating
sending side:
  encapsulates datagram in frame
  adds error checking bits, rdt, flow control, etc.
receiving side
  looks for errors, rdt, flow control, etc.
  extracts datagram, passes to upper layer at receiving side
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame

## Slide 8: Multiple Access Links and LANs
Two types of “links”:
point-to-point, e.g.,
  PPP for dial-up access,
  point-to-point link between Ethernet switch, host
broadcast (shared wire or medium), e.g.
  traditional Ethernet
  802.11 wireless LAN
shared wire (e.g.,
cabled Ethernet)
shared RF
(e.g., 802.11 WiFi)
shared RF
(satellite)
humans at a
cocktail party
(shared air, acoustical)

## Slide 9: LAN: Issues & Technologies
Issues:
  addressing: physical (or MAC) addresses
  media access control (MAC) for broadcast LANs
  expanding LANs: connecting multiple LAN segments
Various commonly used LAN technologies
  Ethernet
  802.11(WiFi)
  PPP

## Slide 10: MAC (Physical, or LAN) Addresses
used to get frames from one interface to another physically-connected interface (same physical network, i.e., p2p or LAN)
48 bit MAC address (for most LANs)
  fixed for each adaptor, burned in the adapter ROM
  MAC address allocation administered by IEEE
    1st bit: 0 unicast, 1 multicast.
    all 1’s : broadcast
MAC flat address -> portability
  can move LAN card from one LAN to another
MAC addressing operations on a LAN:
  each adaptor on the LAN “sees” all frames
  accept a frame if dest. MAC address matches its own MAC address
  accept all broadcast (MAC= all1’s) frames
  accept all frames if set in “promiscuous” mode
  can configure to accept certain multicast addresses (first bit = 1)

## Slide 11: MAC vs. IP Addresses
32-bit IP address:
network-layer address, logical
  i.e., not bound to any physical device, can be re-assigned
IP hierarchical address NOT portable
  depends on IP network to which an interface is attached
  when move to another IP network, IP address re-assigned
used to get IP packets to destination IP network
  Recall how IP datagram forwarding is performed
IP network is “virtual,” actually packet delivery done by the underlying physical networks
  from source host to destination host, hop-by-hop via IP routers
  over each link, different link layer protocol used, with its own frame headers, and source and destination MAC addresses
    Underlying physical networks do not understand IP protocol and datagram format!

## Slide 12: LAN Addresses and ARP
each adapter on LAN has unique LAN address
adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)

## Slide 13: Recall: IP Datagram Forwarding
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Starting at A, given IP datagram addressed to B:
look up net. address of B, find B on same net. as A
link layer send datagram to B inside link-layer frame
B’s MAC
addr
A’s MAC
addr
A’s IP
addr
B’s IP
addr
IP payload
datagram
frame
frame source,
dest address
datagram source,
dest address

## Slide 14: ARP: Address Resolution Protocol
Each IP node (host, router) on LAN has ARP table
ARP Table: IP/MAC address mappings for some LAN nodes
< IP address; MAC address; timer>
  timer: time after which address mapping will be forgotten (typically 20 min)
try out “arp –a” command
Question: how to determine
MAC address of B
knowing B’s IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88

## Slide 15: ARP Protocol
A wants to send datagram to B, and A knows B’s IP address.
A looks up B’s MAC address in its ARP table
Suppose B’s MAC address is not in A’s ARP table.
A broadcasts (why?) ARP query packet, containing B's IP address
  destination MAC address = FF-FF-FF-FF-FF-FF
  all machines on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 16: ARP Messages
Hardware Address Type: e.g., Ethernet
Protocol address Type: e.g., IP
Operation: ARP request or ARP response
Notes: Here is the structure of an ARP packet. Whether it’s a request or reply is specified by the operation.

## Slide 17: ARP Request & Response Processing
The requester broadcasts ARP request
The target node unicasts (why?) ARP reply to requester
  With its physical address
  Adds the requester into its ARP table (why?)
On receiving the response, requester
  updates its table, sets timer
Other nodes upon receiving the ARP request
  Refresh the requester entry if already there
  No action otherwise
Some questions to think about:
  Shall requester buffer IP datagram while performing ARP?
  What shall requester do if never receive any ARP response?
Notes: We can categorize the nodes in the local network into requester node, target node and all others. Lets see what each of them do in turn.
The target node responds only to the sender with its hardware address. Why not broadcast the reply also? All others may not necessarily be interested in communicating with target node and a broadcast incurs processing overhead at every node in the network. The target node adds the requester’s IP and hardware addresses into its ARP cache (if not already there). Why? It is likely that target node would also send IP packets to the requester node later and so it makes sense to avoid an ARP request broadcast by the target node that time.
The requester node on receiving the response, updates its ARP table.
All other nodes, receive only the request not the reply. They check if the requester has an entry in their caches. If found, they refresh that entry. Otherwise, no action taken. Why not add an entry for the requester? We don’t want to grow the ARP table unnecessarily.
Finally, a lifetime is associated with each entry in the ARP cache and an entry is deleted if it not refreshed within that time.

## Slide 18: ARP Operation Illustration
Notes: Here is an illustration of ARP broadcast by W requesting hardware address of Y. As you can see, every node in the local physical network receive this request. Only Y sends the reply and also only to W.

## Slide 19
walkthrough: send datagram from A to B via R
  focus on addressing – at IP (datagram) and MAC layer (frame)
  assume A knows B’s IP address
  assume A knows IP address of first hop router, R (how?)
  assume A knows R’s MAC address (how?)
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
Forwarding to Another LAN

## Slide 20
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame with R's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
Forwarding to Another LAN

## Slide 21
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222
Forwarding to Another LAN

## Slide 22
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy
Forwarding to Another LAN

## Slide 23
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as destination address, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy
Forwarding to Another LAN

## Slide 24
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
Forwarding to Another LAN

## Slide 25: Ethernet Switch
link-layer device: takes an active role
  store, forward Ethernet frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
transparent
  hosts are unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured

## Slide 26: Ethernet Frame Structure
sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
used to synchronize receiver, sender clock rates
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 27: Ethernet Frame Structure (More)
addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g. ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
type: indicates higher layer protocol (mostly IP but others possible, e.g., Novell IPX, AppleTalk)
CRC: cyclic redundancy check at receiver
  error detected: frame is dropped
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 28: Ethernet: Unreliable, Connectionless
connectionless: no handshaking between sending and receiving NICs
unreliable: receiving NIC doesn't send acks or nacks to sending NIC
  data in dropped frames recovered only if initial sender uses higher layer rdt (e.g., TCP), otherwise dropped data lost
Ethernet’s MAC protocol: unslotted CSMA/CD with binary backoff
Will discuss Ethernet MAC CSMA/CD protocol later!

## Slide 29: Switch: Multiple Simultaneous Transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6

## Slide 30: Switch Forwarding Table
Q: how does switch know A’ reachable via interface 4, B’ reachable via interface 5?
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?

## Slide 31: Self Learning
A bridge/switch has a forwarding (or switch) table
entry in forwarding table:
  (MAC Address, Interface, Time Stamp)
  stale entries in table dropped (TTL can be 60 min)
Bridge/switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in forwarding table

## Slide 32
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60
Self-learning, forwarding: example

## Slide 33: Filtering/Forwarding
when frame received at switch:
  1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving
  interface */

## Slide 34: Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
A A’
A A’
A A’
A A’
A A’
frame destination, A’, location unknown:
flood
A’ A
destination A location known:
selectively send
on just one link
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A’
4
60

## Slide 35: Interconnecting switches
self-learning switches can be connected together:
Q: sending from A to G - how does S1 know to forward frame destined to G via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 36: Self-learning multi-switch example
Suppose C sends frame to I, I responds to C
Q: show switch tables and packet forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 37: Spanning Tree Protocol
for increased reliability, desirable to have redundant, alternative paths from source to destination
with multiple paths, cycles result - switches may multiply and forward frame forever
solution: organize switches in a spanning tree by disabling subset of interfaces

## Slide 38: Switch Spanning Tree Algorithm: Algorhyme
I think that I shall never see
A graph more lovely than a tree.
A tree whose crucial property
Is loop-free connectivity.
A tree that must be sure to span
So packets can reach every LAN.
First, the root must be selected.
By ID, it is elected.
Least cost paths from root are traced.
In the tree, these paths are placed.
A mesh is made by folks like me,
Then bridges find a spanning tree
-- Radia Perlman

## Slide 39: Some Switch Features
Isolates collision domains resulting in higher total max throughput
limitless number of nodes and geographical coverage
Can connect different Ethernet types
Transparent (“plug-and-play”): no configuration necessary

## Slide 40: Institutional Network

## Slide 41: Switches vs. Routers
both are store-and-forward:
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
both have forwarding tables:
routers: compute tables using routing algorithms, IP addresses
switches: learn forwarding table using flooding, learning, MAC addresses
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram

## Slide 42: Routers vs. Switches
Switches+ and -
+ Switch operation is simpler requiring less packet processing
+ Switch tables are self learning
- All traffic confined to spanning tree, even when alternative bandwidth is available
- Switches do not offer protection from broadcast storms

## Slide 43: Routers vs. Switches
Routers + and -
+ arbitrary topologies can be supported, cycling is limited by TTL counters (and good routing protocols)
+ provide protection against broadcast storms
- require IP address configuration (not plug and play)
- require higher packet processing
switches do well in small (few hundred hosts) while routers used in large networks (thousands of hosts)