## Slide 1: Network Layer & Network Data Plane Part 1
Network Layer Overview
IPv4 Addressing
  Classful vs. CIDR: network prefixes (w/ “network mask”)
  DHCP
IP Forwarding and IP Protocol
  Briefly: Network Service Models: Datagram vs. Virtual Circuit (we’ll discuss more on Virtual Circuit/MPLS later)
  IP Datagram Forwarding Model: Destination-based Forwarding and Longest Prefix Matching
  Interaction with Data Link Layer (ARP: IP address to MAC address mapping – see slides on data link layer part I)
Readings: Textbook: Chapter 4, Sections 4.1 & 4.3, review section 1.3 (packet vs. circuit switching)

## Slide 2: What Does Network Layer Do?
End-to-end deliver packet from sending to receiving hosts, “hop-by-hop” thru network
  A network-wide concern!
  Involves every router, host in the network
Compare:
  Transport layer
    between two end hosts
  Data link layer
    over a physical link directly connecting two (or more) physically hosts
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 3: What Does Network Layer Do?
transport segment from sending to receiving host
on sending side encapsulates segments into datagrams
on rcving side, delivers segments to transport layer
network layer protocols in every host, router
Router examines header fields in all IP datagrams passing through it
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 4: Network Layer Functions
Addressing
  Globally unique address for each routable device
    Logical address, unlike MAC address (as you’ll see later)
  Assigned by network operator
    Need to map to MAC address (as you’ll see later)
Routing: building a “map” of network
  Which path to use to forward packets from src to dest
Forwarding: delivery of packets hop by hop
  From input port to appropriate output port in a router
  Routing and forwarding depend on network service models: datagram vs. virtual circuit
Notes: The purpose of network layer address is to identify a device and also facilitate routing to that device. It is logical in that it is assigned by the network administrator and can be changed at will unlike the MAC address. We will see later that we need to map these logical addresses to MAC addresses for physical transmission of packets.
Also, we make a distinction between routing and forwarding. Routing is about selecting a path to the destination while forwarding is about moving packets from input ports to appropriate output ports to as per the routing decisions. This distinction may seem subtle and confusing but will become clearer as we go on.

## Slide 5: Two Key Network-Layer Functions
forwarding: move packets from router’s input to appropriate router output
routing: determine route taken by packets from source to dest.
  routing algorithms
analogy:
routing: process of planning trip from source to dest
forwarding: process of getting through single interchange

## Slide 6: Network Layer: Data Plane, Control Plane
Data plane
local, per-router function
determines how datagram arriving on router input port is forwarded to router output port
forwarding function
Control plane
network-wide logic
determines how datagram is routed among routers along end-end path from source host to destination host
two control-plane approaches:
  traditional routing algorithms: implemented in routers
  software-defined networking (SDN): implemented in (remote) servers
1
2
3
0111
values in arriving
packet header

## Slide 7
Per-router Control Plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact in the control plane
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 8
data
plane
control
plane
Logically Centralized Control Plane
A distinct (typically remote) controller interacts with local control agents (CAs)
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header

## Slide 9: Routing & Forwarding: Logical View of a Router
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
Notes: Here is an abstract view of the internals of a typical router. We can separate the functionality of a router into control plane and data plane. The control plane is responsible for exchanging routing information (control packets) with other routers and making routing decisions. Generally, there exists a route processor to process these control packets and to update the routing table. This routing table is then condensed into a form known as forwarding table for quick lookup by the data plane. The job of data plane is to switch packets from input ports to output ports, which is essentially a forwarding.engine. Data packets flow thru this faster data plane while control packets are processed by slower control plane. Another way to look at is that routing decisions are made by control plane and forwarding lookups done by data plane.

## Slide 10: Network Layer Functions
Addressing  IPv4 Addressing
  Globally unique address for each routable device
    Logical address, unlike MAC address (as you’ll see later)
  Assigned by network operator
    Need to map to MAC address (as you’ll see later)
Routing: building a “map” of network
  Which path to use to forward packets from src to dest
Forwarding: delivery of packets hop by hop
  From input port to appropriate output port in a router
Notes: The purpose of network layer address is to identify a device and also facilitate routing to that device. It is logical in that it is assigned by the network administrator and can be changed at will unlike the MAC address. We will see later that we need to map these logical addresses to MAC addresses for physical transmission of packets.
Also, we make a distinction between routing and forwarding. Routing is about selecting a path to the destination while forwarding is about moving packets from input ports to appropriate output ports to as per the routing decisions. This distinction may seem subtle and confusing but will become clearer as we go on.

## Slide 11: IPv4 Addressing: Basics
Globally unique (for “public” IP addresses)
IPv4 address: 32-bit identifier for host, router interface
Interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host may have multiple interfaces
  IP addresses associated with each interface
Dot notation (for ease of human reading)
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 12: IP Addressing: Network vs. Host
Two-level hierarchy
  network part (high order bits)
  host part (low order bits)
What’s a network ?
(from IP address perspective)
  device interfaces with same network part of IP address
  can physically reach each other without intervening router
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2

## Slide 13: “Classful” IP Addressing
32 bits
0
network
host
10
network
host
110
network
host
1110
multicast address
A
B
C
D
class
1.0.0.0 to
127.255.255.255
128.0.0.0 to
191.255.255.255
192.0.0.0 to
223.255.255.255
224.0.0.0 to
239.255.255.255
7
15
23
31
  Disadvantage: inefficient use of address space, address space exhaustion
  e.g., class B net allocated enough addresses for 65K hosts, even if only 2K hosts in that network

## Slide 14: Classless Addressing: CIDR
CIDR: Classless InterDomain Routing
Network portion of address is of arbitrary length
Addresses allocated in contiguous blocks
  Number of addresses assigned always power of 2
Address format: a.b.c.d/x
  x is number of bits in network portion of address
11001000 00010111 00010000 00000000
network
part
host
part
200.23.16.0/23
Notes: Unlike in classfull addressing, under classless addressing, the length of the network portion of an address can be arbitrary. Consequently, it is not possible to figure out the network part from the address alone. We need to supply an additional information (network address mask) for that purpose. Now going back to the previous example, by allotting 11 bits for the host portion and 21 bits for the network portion, we can accommodate 2000 hosts without wasting much address space.

## Slide 15: Special IP Addresses
Network address: host id = all 0’s
Directed broadcast address: host id = all 1’s
Local broadcast address: all 1’s
Local host address (this computer): all 0’s
Loopback address
  network id = 127, any host id (e.g. 127.0.0.1)
Notes: When a packet is sent to a network’s directed broadcast address, a single copy of the packet travels across the internet until it reaches the specified network. The packet is then delivered to all hosts on the network. Local broadcast is limited to a local physical network and is used during system startup by a computer that does not yet know the network number. Address of all 0’s is used to refer to this computer when using startup protocols to figure out its own address. Loopback address is used for testing network applications without sending packets into the network.

## Slide 16: IP Addresses: How to Get One?
Q: How does host get IP address?
“static” assigned: i.e., hard-coded in a file
  Wintel: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config
Dynamically assigned: using DHCP (Dynamic Host Configuration Protocol)
  dynamically get address from as server
  “plug-and-play”

## Slide 17: DHCP: Dynamic Host Configuration Protocol
Goal: allow host to dynamically obtain its IP address from network server when it joins network
  Can renew its lease on address in use
  Allows reuse of addresses (only hold address while connected an “on”
  Support for mobile users who want to join network (more shortly)
DHCP overview:
  host broadcasts “DHCP discover” msg
  DHCP server responds with “DHCP offer” msg
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 18: DHCP Client-Server Scenario
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 19: DHCP Client-Server Scenario
DHCP server: 223.1.2.5
arriving
client
time
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
Lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
Lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
Lifetime: 3600 secs

## Slide 20: DHCP: More Than IP Addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 21: IP Addresses: How to Get One? …
Q: How does network get network part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 22: IP Addressing: the Last Word...
Q: How does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned Names and Numbers
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes

## Slide 23: Recall: Network Layer Functions
Addressing  IPv4 Addressing
  Globally unique address for each routable device
    logical address, unlike MAC address (as you’ll see later)
  Assigned by network operator
    Need to map to MAC address (as you’ll see later)
Routing: building a “map” of network
  Which path to use to forward packets from src to dest
Forwarding: delivery of packets hop by hop
  from input port to an appropriate output port in a router (more on how this is done later!)
How forwarding is done depending on the network “service models”: e.g., datagram vs. virtual circuit
We’ll look at IP datagram forwarding model shortly afterwards!
Notes: The purpose of network layer address is to identify a device and also facilitate routing to that device. It is logical in that it is assigned by the network administrator and can be changed at will unlike the MAC address. We will see later that we need to map these logical addresses to MAC addresses for physical transmission of packets.
Also, we make a distinction between routing and forwarding. Routing is about selecting a path to the destination while forwarding is about moving packets from input ports to appropriate output ports to as per the routing decisions. This distinction may seem subtle and confusing but will become clearer as we go on.

## Slide 24: Network Service Model
Q: What service model for “channel” transporting packets from sender to receiver?
guaranteed bandwidth?
preservation of inter-packet timing (no jitter)?
loss-free delivery?
in-order delivery?
congestion feedback to sender?
?
?
?
virtual circuit
or
datagram?
The most important
abstraction provided
by network layer:
service abstraction

## Slide 25: Network Service Model (cont’d)
Some Possible Examples:
Example services for individual datagrams:
guaranteed delivery
guaranteed delivery with less than 40 msec delay
Example services for a flow of datagrams:
in-order datagram delivery
guaranteed minimum bandwidth to flow
restrictions on changes in inter-packet spacing
CSci4211: Network Layer: Data Plane Part 1

## Slide 26: Network Layer Connection vs. Connectionless Service
datagram network provides network-layer connectionless service
VC network provides network-layer connection service
analogous to the transport-layer services, but:
  service: host-to-host
  generally no choice: network typically provides one or the other
  implementation: in network core
network vs transport layer connection service:
  network: between two hosts, in case of VCs, also involves intervening routers
  transport: between two processes

## Slide 27: Virtual Circuit vs. Datagram
Objective of both: move packets through routers from source to destination
Datagram Model:
  Routing: determine next hop to each destination a priori
  Forwarding: destination address in packet header, used at each hop to look up for next hop
    routes may change during “session”
  analogy: driving, asking directions at every gas station, or based on the road signs at every turn
Virtual Circuit Model:
  Routing: determine a path from source to each destination
  “Call” Set-up: fixed path (“virtual circuit”) set up at “call” setup time, remains fixed thru “call”
  Data Forwarding: each packet carries “tag” or “label” (virtual circuit id, VCI), which determines next hop
  routers maintain ”per-call” state

## Slide 28: Datagram Networks: the Internet model
no call setup at network layer
routers: no state about end-to-end connections
  no network-level concept of “connection”
packets forwarded using destination host address
  packets between same source-dest pair may take different paths, when intermediate routes change!
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Send data
2. Receive data

## Slide 29
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
Interplay Between Routing and Forwarding
CSci4211: Network Layer: Data Plane Part 1

## Slide 30: Forwarding Table
Destination Address Range Link Interface
11001000 00010111 00010000 00000000
through 0
11001000 00010111 00010111 11111111
11001000 00010111 00011000 00000000
through 1
11001000 00010111 00011000 11111111
11001000 00010111 00011001 00000000
through 2
11001000 00010111 00011111 11111111
otherwise 3
4 billion possible entries

## Slide 31: IP Forwarding Table
4 billion possible entries!
(in reality, far less, but can still have millions of “routes”)
forwarding table entry format
destination network next-hop (IP address) link interface
(1st IP address , network mask )
11001000 00010111 00010000 00000000, 200.23.16.1 0
11111111 11111111 11111000 00000000
11001000 00010111 00011000 00000000, - (direct) 1
11111111 11111111 11111111 00000000
11001000 00010111 00011001 00000000, 200.23.25.6 2
11111111 11111111 11111000 00000000
otherwise 128.30.0.1 3

## Slide 32: Route aggregation: Shrinking the forwarding table
“Send me anything
with addresses
beginning
200.23.0.0/20”
200.23.2.0/23
200.23.4.0/23
200.23.14.0/23
UMN
Organization 0
CSE Department
Internet
Organization 1
200.23.6.0/23
Organization 2
.
.
.
.
.
.
Port 1
Port 0
Port 7

## Slide 33: Route aggregation with more specific routes
UMN-FAST has a more specific route to CSE department
“Send me anything
with addresses
beginning
200.23.0.0/20”
200.23.2.0/23
200.23.14.0/23
UMN
Organization 0
CSE Department
Internet
UMN-FAST
“Send me anything
with addresses
beginning
200.23.14.0/23”
200.23.4.0/23
Organization 2
.
.
.
.
.
.

## Slide 34: Longest Prefix Matching
DA: 11001000 00010111 00011000 10101010
Examples
DA: 11001000 00010111 00010110 10100001
interface 0
interface 1
But not interface 2, the 3rd entry
is also a match, but shorter!
Prefix Match
11001000 00010111 00010*** *********
11001000 00010111 00011000 *********
11001000 00010111 00011*** *********
otherwise
Link interface
0
1
2
3
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix matching

## Slide 35: IP Datagram Forwarding Model
IP datagram:
misc
fields
source
IP addr
dest
IP addr
data
datagram remains unchanged, as it travels source to destination
addr fields of interest here
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Dest. Net. next router Nhops
223.1.1 1
223.1.2 223.1.1.4 2
223.1.3 223.1.1.4 2
forwarding table in A

## Slide 36: IP Forwarding: Destination in Same Net
Starting at A, send IP datagram addressed to B:
look up net. address of B in forwarding table
find B is on same net. as A
link layer will send datagram directly to B inside link-layer frame
  B and A are directly connected
misc
fields
223.1.1.1
223.1.1.3
data
Dest. Net. next router Nhops
223.1.1 1
223.1.2 223.1.1.4 2
223.1.3 223.1.1.4 2
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
forwarding table in A

## Slide 37: IP Forwarding: Destination in Diff. Net
Starting at A, dest. E:
look up network address of E in forwarding table
E on different network
  A, E not directly attached
routing table: next hop router to E is 223.1.1.4
link layer sends datagram to router 223.1.1.4 inside link-layer frame
datagram arrives at 223.1.1.4
continued…..
misc
fields
223.1.1.1
223.1.2.3
data
Dest. Net. next router Nhops
223.1.1 1
223.1.2 223.1.1.4 2
223.1.3 223.1.1.4 2
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
forwarding table in A

## Slide 38: IP Forwarding: Destination in Diff. Net …
Arriving at 223.1.4, destined for 223.1.2.2
look up network address of E in router’s forwarding table
E on same network as router’s interface 223.1.2.9
  router, E directly attached
link layer sends datagram to 223.1.2.2 inside link-layer frame via interface 223.1.2.9
datagram arrives at 223.1.2.2!!! (hooray!)
misc
fields
223.1.1.1
223.1.2.3
data
Dest. Net router Nhops interface
223.1.1 - 1 223.1.1.4
223.1.2 - 1 223.1.2.9
223.1.3 - 1 223.1.3.27
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
forwarding table in router

## Slide 39: IP Forwarding & IP/ICMP Protocol
Network
layer
forwarding
table
Routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
Datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
Transport layer: TCP, UDP
Data Link layer (Ethernet, WiFi, PPP, …)
Physical Layer (SONET, …)
Notes: This shows the different components of network layer under Internet protocol stack. IP protocol is concerned with addressing and packet forwarding.
The routing table itself is either setup manually or using routing protocols such as Routing Information Protocol (RIP), Open Shortest Path First (OSPF) and Border Gateway Protocol (BGP). These protocols are used to exchange information about the network between routers and update routing tables in response to link and node failures.
Internet Control Message Protocol (ICMP) is for reporting errors such as destination not reachable, number of hops exceeded the specified maximum etc.

## Slide 40: IP Datagram Format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
Internet
checksum
time to
live
32 bit source IP address
IP protocol version
number
header length
(bytes)
max number
remaining hops
(decremented at
each router)
total datagram
length (bytes)
upper layer protocol
to deliver payload to
head.
len
type of
service
“type” of data
flgs
fragment
offset
upper
layer
32 bit destination IP address
Options (if any)
E.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead with TCP?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 41: Fields in IP Datagram
IP protocol version: current version is 4, IPv4, new: IPv6
Header length: number of 32-bit words in the header
Type of Service:
  3-bit priority,e.g, delay, throughput, reliability bits, …
Total length: including header (maximum 65535 bytes)
Identification: all fragments of a packet have same identification
Flags: don’t fragment, more fragments
Fragment offset: where in the original packet (count in 8 byte units)
Time to live: maximum life time of a packet
Protocol Type: e.g., ICMP, TCP, UDP etc
IP Option: non-default processing, e.g., IP source routing option, etc.
Will come back to discuss more about some of these headers!

## Slide 42: Interaction w/ Data Link Layer
We now take a detour from the network layer and dive into the data link layer now, so that we can understand how IP datagrams within the same IP subnet are actually delivered “directly” by the data link layer (which uses only MAC addresses for forwarding!), see the data link layer part 1 slides
We’ll provide a quick overview of data link layer
We will learn about MAC addresses
How IP addresses are mapped to MAC addresses via the ARP protocol
How layer-2 switches (e.g., Ethernet switches or “bridges”) learn and build “switch tables” and forward packets !