## Slide 1: Network Data Plane Part 2
Router/Switch Architecture Overview
Generalization of IP Router and Ethernet Switch Data Plane Operations
  “match-action” forwarding abstraction
Openflow and Software-Defined Networking (SDN)
  Openflow switches
  Openflow protocol: control messages
  SDN controller (POX)
Software Switch (OVS) and Mininet
Readings: Textbook: Chapter 4: Sections 4.2 and 4.4; Chapter 5: Section 5.5 (in particular, Section 5.5.2)

## Slide 2: Recall: Network Layer Functions
Addressing
  Globally unique address for each routable device
Routing: building a “map” of network
  Which path to use to forward packets from src to dest
Forwarding: delivery of packets hop by hop
  from input port to appropriate output port in a router
Forwarding is the “data plane” operation (often performed by “specialized” hardware
–-- we have learned:
  how IP routers forward IP datagrams based on destination IP addresses
  how layer 2 switches forward (Ethernet) frames based on destination MAC addresses
 now let’s examine how it is done in hardware in general (whether in layer-2 switches or layer-3 routers)

## Slide 3: Router/Switch Architecture Overview
A key router/switch data plane function:
forwarding packets (e.g., IP datagrams, or Ethernet frames) from incoming to outgoing link (or drop them if no forwarding table entries, or flood them if no switching table entries
General CPU
NICs -- special hardware (ASICs)
varies depending on
“generations”
forwarding
operations
control
operations

## Slide 4: Input Port Functions
Decentralized switching:
using header field values, lookup output port using forwarding table in input port memory
goal: complete input port processing at ‘line speed’
queuing: if datagrams arrive faster than forwarding rate into switch fabric
Physical layer:
bit-level reception
Data link layer:
e.g., Ethernet
see chapter 6

## Slide 5: Switching Fabrics
memory
memory
bus
crossbar
transfer packet from input buffer to appropriate output buffer
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
three types of switching fabrics

## Slide 6: Switching Via Memory
First generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus

## Slide 7: Switching Via a Bus
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access and enterprise routers

## Slide 8: Switching Via An Interconnection Network
overcome bus bandwidth limitations
banyan networks, crossbar, other interconnection nets initially developed to connect processors in multiprocessor
advanced design: fragmenting datagram into fixed length cells, switch cells through the fabric.
Cisco 12000: switches 60 Gbps through the interconnection network

## Slide 9: Input Port Queuing
Fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
output port contention:
only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric

## Slide 10: Output Ports
Buffering required when datagrams arrive from fabric faster than the transmission rate
Scheduling discipline chooses among queued datagrams for transmission
Datagram (packets) can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance, network neutrality

## Slide 11: Output Port Queueing
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric

## Slide 12: Router/Switch Data Plane Operations: Forwarding Abstraction
We have learned:
How IP routers forward IP datagrams based on destination IP addresses
  take the dest. IP address from an IP packet
  look up the IP forwarding table using the longest prefix matching
  if there’s a match, forwarding the packet to the outgoing port specified; otherwise drop it
How layer 2 switches forward (Ethernet) frames based on destination MAC addresses
  take the dest. MAC address from an Ethernet frame
  look up the switch table using the exact matching
  if there’s a match, forwarding the packet to the outgoing port specified; otherwise flood it to all other ports
What are common and what are different?
  Common: match a header field against a table, then take an action
  Different: how table is constructed, what header fields to match, how to match it, and what actions to take

## Slide 13: Router/Switch Data Plane Operations: Forwarding Abstraction
We have learned:
How IP routers forward IP datagrams based on destination IP addresses
  take the dest. IP address from an IP packet
  look up the IP forwarding table using the longest prefix matching
  if there’s a match, forwarding the packet to the outgoing port specified; otherwise drop it
How layer 2 switches forward (Ethernet) frames based on destination MAC addresses
  take the dest. MAC address from an Ethernet frame
  look up the switch table using the exact matching
  if there’s a match, forwarding the packet to the outgoing port specified; otherwise flood it to all other ports
What are common and what are different?
  Common: match a header field against a table, then take an action
  Different: how table is constructed, what header fields to match, how to match it, and what actions to take
“Hardware” components (forwarding operations – match via table lookup, actions, etc. ) are (nearly) the same;
“Software” computations (how tables/rules are configured) differ
That’s why you can buy a generic WiFi router/modem from Best Buy, and configure it either as a WiFi IP router (layer 3 device), or simply as a WiFI LAN switch (layer 2 device)!

## Slide 14
2
3
0100 1101
values in arriving
packet’s header
logically-centralized routing controller
1
control plane
data plane
Each switch contains a flow table that is computed and distributed by a logically centralized routing controller
local flow table
headers counters actions
Generalized Forwarding and SDN

## Slide 15: OpenFlow data plane abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  Pattern: match values in packet header fields
  Actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
Flow table in a router (computed and distributed by controller) define router’s match+action rules

## Slide 16
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  Pattern: match values in packet header fields
  Actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller
* : wildcard
OpenFlow data plane abstraction

## Slide 17: OpenFlow: Flow Table Entries
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Rule
Action
Stats
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
Modify Fields
Packet + byte counters
Link layer
Network layer
Transport layer
Notes: Now I’ll describe the API that tries to meet these goals.
17

## Slide 18
Destination-based forwarding:
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
51.6.0.8
*
*
*
port6
IP datagrams destined to IP address 51.6.0.8 should be forwarded to router output port 6
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
*
*
*
*
22
drop
Firewall:
do not forward (block) all datagrams destined to TCP port 22
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
128.119.1.1
*
*
*
*
drop
do not forward (block) all datagrams sent by host 128.119.1.1
Examples

## Slide 19: OpenFlow Abstraction
IP Router
  match: longest destination IP prefix
  action: forward out a link
Layer-2 (Ethernet) Switch
  match: destination MAC address
  action: forward or flood
Firewall
  match: IP addresses and TCP/UDP port numbers
  action: permit or deny
NAT
  match: IP address and port
  action: rewrite address and port
match+action: unifies the data-plane operations of different kinds of routers, switches, and other devices

## Slide 20: OpenFlow example
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(3)
match
action
ingress port = 2
IP Dst = 10.2.0.3
ingress port = 2
IP Dst = 10.2.0.4
forward(3)
match
action
forward(4)
ingress port = 1
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(4)
match
action
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Example: datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2

## Slide 21: Traditional Network Devices
L3 Router
If dst-ip == X then
ttl = ttl – 1
checksum = updateChecksum(packet)
dst-mac = xx:xx:xx:xx:xx:xx
send to output port P
end
Data Plane
Control Plane
Data Plane
Control Plane
Data Plane
Control Plane
Data Plane
Control Plane
Data Plane
Control Plane
Data Plane
Control Plane
Packet

## Slide 22: Simple SDN Network
Switch
Host1
Host2
Controller
L2 Forwarding
Controller APIs
Communication Protocol
Ethernet,IP,ARP,TCP,HTTP,…
POX, Floodlight, …
Software or Hardware

## Slide 23: Communication Protocol (OpenFlow)

## Slide 24: OpenFlow (Main Components)
Flow tables
  Matching
  Manipulation
  Counters
Communication messages
  Controller to switch
  Asynchronous
  Symmetric
Controller
Pipeline
Secure Channel
Flow Table
Flow Table

## Slide 25: Flow Tables (Structure)
A flow-table consists of
  a set of flow entries
  a table miss configuration
    Drop packet
    Send to controller
    Process using the next flow-table
Match fields | Counters | Instructions

## Slide 26: Flow Tables (Processing)
Pipeline processing
Per table processing
  Find highest-priority matching ﬂow entry
  Apply instructions
    Modify packet & update match fields
    Update action set
    Update metadata
  Send match data and action set to next table

## Slide 27: Flow Tables (Matching)
Physical  Ingress port
Metadata
L2  MAC src/dst, EtherType, VLAN, MPLS
L3  IP src/dst, IP proto, IP ToS, ARP code
L4  TCP/UDP src/dst, ICMP

## Slide 28: Flow Tables (Counters)
Table counters
  e.g. Packet lookups/matches
Flow counters
  e.g. packets/bytes received
Port counters
  e.g. packets/bytes transmitted/received, drops

## Slide 29: Flow Tables (Instructions)
Apply actions Apply the specified list action(s) immediately without modifying the action set
Clear actions Clear all actions in the action set immediately
Write actions Merge the specified set action(s) to the action set
Write metadata Write the specified bits to the metadata register
Goto table Indicate the next-table in the pipeline

## Slide 30: Flow Tables (Actions)
Output
  IN_PORT  send packet to ingress port
  CONTROLLER  encapsulate and send to controller
  FLOOD  send packet to ports except ingress port
Drop
Push/Pop VLAN/MPLS tag
Set-Field
  IPv4 src/dst addresses
  MAC src/dst addresses
  TCP src/dst ports

## Slide 31: Communication Messages (Controller to Switch)
Features Switch replies with list of ports, ports speeds, supported tables and actions
Modify state Add, delete, or modify flow tables
Read state Controller queries table, flow, or port counters
Packet out Used by controller to send packets out of a specified port on the switch
Barrier Used to ensure message dependencies have been met

## Slide 32: Communication Messages (Asynchronous)
Packet in All packets that do not have a matching flow entry are encapsulated and sent to the controller
Flow removed Sent to controller when flow expires due to idle or hard timeouts
Port status Generated if a port is brought down

## Slide 33: Communication Messages (Symmetric)
Hello Sent during the handshake i.e. secure channel setup
Echo Sent to verify liveness and measure channel latency

## Slide 34: SDN Controller (POX)

## Slide 35: POX
SDN controller written in Python
Many build-in modules
Python APIs to enable user extensions

## Slide 36: POX (Built-in Modules)
Hub flood packets
L2 forwarding MAC learning
L3 forwarding IP learning
Topology discovery Underlying topology discovery
Spanning tree protocol Implementation of the standard STP
…

## Slide 37: POX (Python APIs)
Publish-Subscribe system
A module can raise events
A module can register for events provides by other modules
A module must have a launch function

## Slide 38: POX (Python APIs)
Event Management
openflow
L2 forwarding
Switch
Switch
POX Core
Handle
PacketIN
Packet
Raise PacketIn
Event
Firewall
Handle
PacketIN
(priority=100)
Packet
Packet
Register
Register

## Slide 39: POX (Python APIs)

## Slide 40: Software Switch (Open vSwitch)

## Slide 41: Open vSwitch (In a Nutshell)

## Slide 42: L2 Switching
MAC learning
VLANs (will be discussed later)
  Learning table per VLAN ID
  Packets can only be forwarded between ports with the same VLAN ID

## Slide 43: Open vSwitch (Features)
Enables Linux to become part of the SDN architecture
Features
  L2-L4 matching
  VLANs with trunking
  Tunneling protocols such as GRE
  Remote configuration protocol
  Multi-table forwarding pipeline
  Monitoring via NetFlow, sFlow
  Spanning Tree Protocol
  Fine-grained QoS
  OpenFlow support
Runs in either
  Standalone mode
  OpenFlow mode

## Slide 44: Open vSwitch (Configuration)
Add a bridge and connect to controller
Host 1
VM1
br1
eth0
eth1
tap0
eth2
SDN
Controller

## Slide 45: Open vSwitch (Configuration)
Add a bridge and connect to controller

## Slide 46: A Network in a Laptop (Mininet)

## Slide 47: Mininet
Mininet is a system for rapidly prototyping large networks on a single laptop
Lightweight OS-level virtualization
  Isolated network namespace
  Constrained CPU usage on isolated namespace
CLI and Python APIs
Can
  Create custom topologies
  Run real programs
  Custom packet forwarding using OpenFlow

## Slide 48: Mininet (Architecture)

## Slide 49: Mininet (Examples)

## Slide 50: References
OpenFlow http://www.openflow.org
Open vSwitch http://www.openvswitch.org
POX https://openflow.stanford.edu/display/ONL/POX+Wiki
Mininet http://mininet.org