## Slide 1: Network Data Plane Part 3
Miscellaneous topics related to network layer (IP) data plane (and VLAN)
Link/Path MTU and IPv4 Fragmentation and Reassembly
NAT (network address translation)
IPv6 and IPv6 Transition
Virtual Circuit and MPLS
VLAN
Readings: Textbook: Chapter 4, Sections 4.3.1-4.3.2, 4.3.4-4.3.5; Chapter 5: Section 5.6; Chapter 6: Sections 6.4.4 & Section 6.5; Section 6.7

## Slide 2: IP Forwarding & IP/ICMP Protocol
Network
layer
forwarding
table
Routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
Datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
Transport layer: TCP, UDP
Data Link layer (Ethernet, WiFi, PPP, …)
Physical Layer (SONET, …)
Notes: This shows the different components of network layer under Internet protocol stack. IP protocol is concerned with addressing and packet forwarding.
The routing table itself is either setup manually or using routing protocols such as Routing Information Protocol (RIP), Open Shortest Path First (OSPF) and Border Gateway Protocol (BGP). These protocols are used to exchange information about the network between routers and update routing tables in response to link and node failures.
Internet Control Message Protocol (ICMP) is for reporting errors such as destination not reachable, number of hops exceeded the specified maximum etc.

## Slide 3: IP Datagram Format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
Internet
checksum
time to
live
32 bit source IP address
IP protocol version
number
header length
(bytes)
max number
remaining hops
(decremented at
each router)
for
fragmentation/
reassembly
total datagram
length (bytes)
upper layer protocol
to deliver payload to
head.
len
type of
service
“type” of data
flgs
fragment
offset
upper
layer
32 bit destination IP address
Options (if any)
E.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead with TCP?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 4: Fields in IP Datagram
IP protocol version: current version is 4, IPv4, new: IPv6
Header length: number of 32-bit words in the header
Type of Service:
  3-bit priority,e.g, delay, throughput, reliability bits, …
Total length: including header (maximum 65535 bytes)
Identification: all fragments of a packet have same identification
Flags: don’t fragment, more fragments
Fragment offset: where in the original packet (count in 8 byte units)
Time to live: maximum life time of a packet
Protocol Type: e.g., ICMP, TCP, UDP etc
IP Option: non-default processing, e.g., IP source routing option, etc.

## Slide 5: IP Fragmentation & Reassembly: Why
network links have MTU (max.transfer size) - largest possible link-level frame.
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly

## Slide 6: IP Fragmentation & Reassembly: How
An IP datagram is chopped by a router into smaller pieces if
  datagram size is greater than network MTU
  Don’t fragment option is not set
Each datagram has unique datagram identification
  Generated by source hosts
  All fragments of a packet carry original datagram id
All fragments except the last have more flag set
  Fragment offset and Length fields are modified appropriately
Fragments of IP packet can be further fragmented by other routers along the way to destination !
Reassembly only done at destination host (why?)
  Use IP datagram id, fragment offset, fragment flags. Length
  A timer is set when first fragment is received (why?)

## Slide 7: IP Fragmentation and Reassembly: Exp
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
One large datagram becomes
several smaller datagrams
Example
4000 byte datagram
MTU = 1500 bytes
offset in the second fragment:
185x8=1480
(why not 1500 bytes =length?)
offset in the third fragment:
370x8=2960
  Except for last fragment, IP fragment payload size (i.e., excluding IP header) must be multiple of 8!

## Slide 8: Quiz: Calculating length & Offset
ID
=x
offset
=0
fragflag
=0
length
=4000
Example
4000 byte datagram
MTU = 1500 bytes
A
B
MTU = 1500 bytes
MTU = 900 bytes

## Slide 9: Answer
ID
=x
Offset
= 0
fragflag
=1
length
= 900
ID
=x
offset
=110
fragflag
=1
length
=620
ID
=x
offset
= 185
fragflag
=1
length
= 900
ID
=x
offset
= 295
fragflag
=1
length
= 620
ID
=x
offset
=370
fragflag
=1
length
= 900
ID
=x
offset
= 480
fragflag
=0
length
= 160

## Slide 10: ICMP: Internet Control Message Protocol
used by hosts, routers, gateways to communication network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 dest port unreachable
3 4 datagram too big
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
5 0,1 redirect for network/host
8 0 echo request (ping)
9 0 route advertisement
10 0 router solicitation
11 0 TTL expired
12 0 bad IP header

## Slide 11: ICMP Message Transport & Usage
ICMP messages carried in IP datagrams
Treated like any other datagrams
  But no error message sent if ICMP message causes error
Message sent to the source
  8 bytes of the original header included
ICMP Usage (non-error, informational): Examples
  Testing reachability: ICMP echo request/reply
    ping
  Tracing route to a destination: Time-to-live field
    traceroute
  Path MTU discovery (see next slide for more details)
    Don’t fragment bit
  IP redirect (for hosts only): inform hosts of better routes
Notes: The protocols IP and ICMP are co-dependent. IP uses ICMP to report error messages and ICMP uses IP to transport messages. ICMP messages are treated like any other datagrams with one exception. If a datagram carrying an ICMP error message causes an error, no error message is sent. Obviously, we want to avoid an internet from becoming congested carrying error messages about error messages.
Where should an ICMP message be sent? ICMP messages are always created in response to a datagram. ICMP message is sent back to the source IP address in the datagram.

## Slide 12: ICMP and Path MTU (RFC 1191)
When a router is unable to forward a datagram, because it exceeds the MTU of the next-hop network and its “Don't Fragment” bit is set, the router is required to
return an ICMP “Destination Unreachable” message (type 3) to the source of the datagram, with code 4, indicating ”Fragmentation required and DF flag set".
To support Path MTU Discovery, the router MUST
include the MTU of that next-hop network in the low-order 16 bits of the ICMP header field that is labelled "unused" in the ICMP specification.
The high-order 16 bits remain unused, and MUST be set to zero.

## Slide 13
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0.0/24
rest of
Internet
datagrams with source or
destination in this network
have 10.0.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,different source port numbers
NAT (Network Address Translation) A fix to limited IPv4 address space:

## Slide 14
motivation: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net not explicitly addressable, visible by outside world (a security plus)
NAT (Network Address Translation)

## Slide 15
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345
NAT (Network Address Translation)

## Slide 16: IPv6: Motivation
initial motivation: 32-bit address space soon to be completely allocated.
additional motivation:
  header format helps speed processing/forwarding
  header changes to facilitate QoS
IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed --- hosts must perform path MTU discovery to learn about path MTU!

## Slide 17: Simplified Design of IPv6
No checksum operation
No fragmentation
Longer addressing space
Fix size IP Header
2001:0db8:85a3:0000:0000:8a2e:0370:7334
Can have one or more
extension header fields
End hosts must perform path MTU
discovery (using ICMP) per destination
before sending any data!
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits

## Slide 18: IPv6 Transition
Dual stack hosts
  Two TCP/IP stacks co-exists on one host
  Supporting IPv4 and IPv6
  Client uses whichever protocol it wishes
IPv4
IPv6
www.apnic.net
?
?
IPv4
TCP/UDP
Application
IPv6
Link

## Slide 19: IPv6 Transition (cont’d)
IPv6 tunnel over IPv4
IPv4
Network
IPv6
IPv6
IPv6 Header
Data
IPv4 Header
IPv6 Header
Data
IPv6 Header
Data
tunnel

## Slide 20: Tunnels and “Network Virtualization” Techniques
IPv6 tunnels over IPv4 provides an example of the general way that one type of networks can be used to support another type of networks to, e.g., support incremental deployment of a new protocol, accommodate the co-existence of multiple (heterogeneous) networks, or implement “network virtualization” (e.g., a “private network” running on top of a public Internet)
IP-in-IP tunnels
  IPv6-in-IPv4 tunnels or IPv4-in-IPv6 tunnels
  IPv4-in=IPv4 tunnels, e.g., virtual private network (VPN)
Virtual Circuits as tunnels in IP networks
  e.g., MPLS (multiple protocol label switching) is often used to form virtual IP “links” (across multiple IP routers)
VLAN (layer-2 virtual LAN); VxLAN (virtual LANs over UDP/IP)
GRE, L2TP, and other tunnels; application-layer gateways; …...
Note: impact on MTU !

## Slide 21: Virtual Circuit vs. Datagram
Objective of both: move packets through routers from source to destination
Datagram Model:
  Routing: determine next hop to each destination a priori
  Forwarding: destination address in packet header, used at each hop to look up for next hop
    routes may change during “session”
  analogy: driving, asking directions at every gas station, or based on the road signs at every turn
Virtual Circuit Model:
  Routing: determine a path from source to each destination
  “Call” Set-up: fixed path (“virtual circuit”) set up at “call” setup time, remains fixed thru “call”
  Data Forwarding: each packet carries “tag” or “label” (virtual circuit id, VCI), which determines next hop
  routers maintain ”per-call” state

## Slide 22: Virtual Circuits
call setup/teardown for each call before data can flow
  need special control protocol: “signaling”
  every router on source-dest path maintains “state” (VCI translation table) for each passing call
  VCI translation table at routers along the path of a call “weaving together” a “logical connection” for the call
link, router resources (bandwidth, buffers) may be reserved and allocated to each VC
  to get “circuit-like” performance
Compare w/ transport-layer “connection”: only involves two end systems, no fixed path, can’t reserve bandwidth!
“source-to-dest path behaves much like telephone circuit” (but actually over packet network)
  performance-wise
  network actions along source-to-dest path

## Slide 23: VC Implementation
a VC consists of:
  path from source to destination
  VC numbers, one number for each link along path
  entries in forwarding tables in routers along path
packet belonging to VC carries VC number (rather than dest address)
VC number can be changed on each link.
  New VC number comes from forwarding table

## Slide 24: VC Translation/Forwarding Table
12
22
32
1
2
3
VC number
interface
number
Incoming interface Incoming VC # Outgoing interface Outgoing VC #
1 12 3 22
2 63 1 18
3 7 2 17
1 97 3 87
… … … …
Forwarding table in
northwest router:
Routers maintain connection state information!

## Slide 25: Virtual Circuit: Signaling Protocols
used to setup, maintain teardown VC
used in ATM, frame-relay, X.25
used in part of today’s Internet: Multi-Protocol Label Switching (MPLS) operated at “layer 2+1/2” (between data link layer and network layer) for “traffic engineering” purpose
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Initiate call
2. incoming call
3. Accept call
4. Call connected
5. Data flow begins
6. Receive data

## Slide 26: Virtual Circuit Setup/Teardown
Call Set-Up:
Source: select a path from source to destination
  Use routing table (which provides a “map of network”)
Source: send VC setup request control (“signaling”) packet
  Specify path for the call, and also the (initial) output VCI
  perhaps also resources to be reserved, if supported
Each router along the path:
  Determine output port and choose a (local) output VCI for the call
    need to ensure that NO two distinct VCs leaving the same output port have the same VCI!
  Update VCI translation table (“forwarding table”)
    add an entry, establishing an mapping between incoming VCI & port no. and outgoing VCI & port no. for the call
Call Tear-Down: similar, but remove entry instead
Notes: Previously we were talking about how to forward packets once the virtual circuit has been set up. For setting a VC, a source has to first select a path and send setup request along that path. We will see later how a source can get information about the network and perform path selection. Each router along the path choose a local VCI for the connection. To be precise, a downstream router selects a VCI to be used as output VCI by the upstream node. Basically we have to make sure that two distinct VCs do not have the same VCI when they flow thru the same port. Once the VCI is chosen, forwarding table is updated to reflect the new mapping from an incoming VCI and port no to outgoing VCI and port no. VC setup is essentially the updation of forwarding tables along a selected path.
The key thing to note here is that VCI has only local significance and that’s why VCI of a packet is changed at each router along the path. If we want VCI to have global meaning, then we would need a larger VCI to identify every connection in the whole network. Moreover, we need to ensure that each VCI is globally unique. On the other hand, with local VCIs a router has to worry only about the VCs passing thru itself which will be much fewer. Also, some other router can also use the same VCI as long as two VCs do not get switched to the same port with same VCI. So with a smaller VCI also it is possible to have many connections in the network.
Another thing to note here is the difference between routing and forwarding. Here the path selection is done the VC setup time, i.e., routing decision is made before any data is sent. And forwarding table along the selected path are updated as part of VC setup. After that each packet gets forwarded by each router/switch along the path as per the routing decision made at the time of VC setup.

## Slide 27
During data packet forwarding phase, input VCI is used to look up the table, and is “swapped” w/ output VCI (VCI translation, or “label swapping”)
VCI translation table (aka “forwarding table”), built at call set-up phase
1
2
1
3
1
2
2
1
four “calls” going thru the router, each entry corresponding one call
green call
purple call
blue call
orange call
Notes: Here is an example of how VCI translation is done. Forwarding table maps a packet from an input port with input VCI to an output port and output VCI. This forwarding table is set up such that no two packets belonging to different connections (with different input VCIs or from different input ports) get switched to the same output port with same output VCI.
In this example, forwarding table says that a packet coming thru input port 1 with VCI 2 should be sent out on port 4 and VCI of the packet be changed to 1. Similarly packets from port 2 with VCI 1 are sent out on port 3 with VCI 2. You can see that no two output VCIs are same if the output port is also same.

## Slide 28: Virtual Circuit: Example
0
1
3
2
0
1
3
2
0
1
3
2
5
11
4
7
Router 3
Host B
Router 2
Host A
Router 1
Router 4
“call” from host A to host B along path:
host A router 1 router 2  router 3  host B
each router along path maintains an entry for the call in its VCI translation table
the entries piece together a “logical connection” for the call
Exercise: write down the VCI translation table entry for the call at each router

## Slide 29: Multiprotocol Label Switching (MPLS)
initial goal: speed up IP forwarding by using fixed length label (instead of IP address) to do forwarding
  borrowing ideas from Virtual Circuit (VC) approach
  but IP datagram still keeps IP address!
PPP or Ethernet
header
IP header
remainder of link-layer frame
MPLS header
label
Exp
S
TTL
20
3
1
8

## Slide 30: MPLS Capable Routers
a.k.a. label-switched router
forward packets to outgoing interface based only on label value (don’t inspect IP address)
  MPLS forwarding table distinct from IP forwarding tables
flexibility: MPLS forwarding decisions can differ from those of IP
  use destination and source addresses to route flows to same destination differently (traffic engineering)
  re-route flows quickly if link fails: pre-computed backup paths (useful for VoIP)

## Slide 31: MPLS versus IP paths
R2
D
R3
R5
A
R6
IP router
IP routing: path to destination determined by destination address alone
R4

## Slide 32: MPLS versus IP paths
R2
D
R3
R4
R5
A
R6
IP-only
router
IP routing: path to destination determined by destination address alone
MPLS and
IP router
MPLS routing: path to destination can be based on source and destination address
  fast reroute: precompute backup routes in case of link failure
entry router (R4) can use different MPLS routes to A based, e.g., on source address

## Slide 33: MPLS Signaling
modify OSPF, IS-IS link-state flooding protocols to carry info used by MPLS routing,
  e.g., link bandwidth, amount of “reserved” link bandwidth
D
R4
R5
A
R6
entry MPLS router uses RSVP-TE signaling protocol to set up MPLS forwarding at downstream routers
modified
link state
flooding
RSVP-TE

## Slide 34: MPLS Forwarding Tables
R1
R2
D
R3
R4
R5
0
1
0
0
A
R6
in out out
label label dest interface
6 - A 0
in out out
label label dest interface
10 6 A 1
12 9 D 0
in out out
label label dest interface
10 A 0
12 D 0
1
in out out
label label dest interface
8 6 A 0
0
8 A 1

## Slide 35: VLANs: Motivation
consider:
CS user moves office to EE, but wants connect to CS switch?
single broadcast domain:
  all layer-2 broadcast traffic (ARP, DHCP, unknown location of destination MAC address) must cross entire LAN
  security/privacy, efficiency issues
Computer
Science
Electrical
Engineering
Computer
Engineering

## Slide 36: VLANs
port-based VLAN: switch ports grouped (by switch management software) so that single physical switch ……
switch(es) supporting VLAN capabilities can be configured to define multiple virtual LANS over single physical LAN infrastructure.
Virtual Local
Area Network
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
Electrical Engineering
(VLAN ports 1-8)
…
1
8
2
7
9
16
10
15
…
Computer Science
(VLAN ports 9-16)
… operates as multiple virtual switches

## Slide 37: Port-based VLAN
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
traffic isolation: frames to/from ports 1-8 can only reach ports 1-8
  can also define VLAN based on MAC addresses of endpoints, rather than switch port
dynamic membership: ports can be dynamically assigned among VLANs
router
forwarding between VLANS: done via routing (just as with separate switches)
  in practice vendors sell combined switches plus routers

## Slide 38: VLANs Spanning Multiple Switches
trunk port: carries frames between VLANS defined over multiple physical switches
  frames forwarded within VLAN between switches can’t be vanilla 802.1 frames (must carry VLAN ID info)
  802.1q protocol adds/removed additional header fields for frames forwarded between trunk ports
1
8
9
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
2
7
3
Ports 2,3,5 belong to EE VLAN
Ports 4,6,7,8 belong to CS VLAN
5
4
6
8
16
1
CSci4211: Network Data Plane Part 3

## Slide 39
type
2-byte Tag Protocol Identifier
(value: 81-00)
Tag Control Information (12 bit VLAN ID field,
3 bit priority field like IP TOS)
Recomputed
CRC
802.1Q VLAN frame format
802.1 frame
802.1Q frame
dest.
address
source
address
data (payload)
CRC
preamble
dest.
address
source
address
preamble
data (payload)
CRC
type

## Slide 40: NAT, MPLS, VLAN and OpenFlow Switches
How do you realize NAT, MPLS and VLAN operations using an OpenFlow switch?
In other words, what should be the “match-action” rules?
  What fields to match?
  What actions to take?
Switch
Port
MAC
src
MAC
dst
Eth
type
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
MPLS
Label
VLAN
ID

## Slide 41: A day in the life: scenario
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
web page
browser

## Slide 42: A day in the life… connecting to the Internet
router
(runs DHCP)
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP

## Slide 43: A day in the life… connecting to the Internet
router
(runs DHCP)
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply

## Slide 44: A day in the life… ARP (before DNS, before HTTP)
router
(runs DHCP)
before sending HTTP request, need IP address of www.google.com: DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
Eth
Phy
ARP
ARP
ARP reply

## Slide 45: A day in the life… using DNS
router
(runs DHCP)
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into Comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
demuxed to DNS server
DNS server replies to client with IP address of www.google.com
Comcast network
68.80.0.0/13
DNS server
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS

## Slide 46: A day in the life…TCP connection carrying HTTP
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in 3-way handshake) inter-domain routed to web server
TCP connection established!
64.233.169.105
web server
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK (step 2 in 3-way handshake)

## Slide 47: A day in the life… HTTP request/reply
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
64.233.169.105
web server
HTTP
TCP
IP
Eth
Phy
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed